Birdhouse
2022/04/01 Ben Larcher
www.graineahumus.org
Version 0.1

Blueprints for various species

# Cutting

Exploded view of the birdhouse.

To save wood, these blueprints can be made with a single board.

# Sizes
Piece size varies by species. Here is a summary table of sizes.

## Type 1
For eurasian blue tit, marsh tit, european crested tit or coal tit
	Dimensions (in cm)
1-Removable roof	17 + e (depth) / 18 + 2 e (width)
2 et 3-Sides	14 (width) / 25 - e (front side) / 28 - e (back side)
4-Bottom	14 (depth) / 14 + 2 e (width)
5-Front with hole	25 (height) / 14 + 2 e (width) / 28 mm diameter hole
6-Back	35 (height) / 14 + 2 e (width)

e is the thickness. If the board is 1.8 cm thick, then 2 e = 1.8 x 2 = 3.6 cm.

## Type 2
For great tit, tree sparrow, pied flycatcher
	Dimensions (in cm)
1-Removable roof	17 + e (depth) / 18 + 2 e (width)
2 et 3-Sides	14 (width) / 25 - e (front side) / 28 - e (back side)
4-Bottom	14 (depth) / 14 + 2 e (width)
5-Front with hole	25 (height) / 14 + 2 e (width) / 32 mm diameter hole
6-Back	35 (height) / 14 + 2 e (width)

e is the thickness. If the board is 1.8 cm thick, then 2 e = 1.8 x 2 = 3.6 cm.

Only the front hole changes from the previous dimensions.
By opting for this size, it is likely that species from the previous blueprint will live there, given the small differences.

## Type 3
For Eurasian nuthatch, common redstart
	Dimensions (in cm)
1-Removable roof	17 + e (depth) / 18 + 2 e (width)
2 et 3-Sides	14 (width) / 25 - e (front side) / 28 - e (back side)
4-Bottom	14 (depth) / 14 + 2 e (width)
5-Front with hole	25 (height) / 14 + 2 e (width) / Oval hole 32mm wide by 48mm high
6-Back	35 (height) / 14 + 2 e (width)

e is the thickness. If the board is 1.8 cm thick, then 2 e = 1.8 x 2 = 3.6 cm.

## Type 4
For common starling
	Dimensions (in cm)
1-Removable roof	19,5 + e (depth) / 20 + 2 e (width)
2 et 3-Sides	16 (width) / 30 - e (front side) / 34 - e (back side)
4-Bottom	16 (depth) / 16 + 2 e (width)
5-Front with hole	30 (height) / 16 + 2 e (width) / Oval hole 45mm wide by 50mm high
6-Back	41 (height) / 14 + 2 e (width)

e is the thickness. If the board is 1.8 cm thick, then 2 e = 1.8 x 2 = 3.6 cm.

## Type 5
For Eurasian hoopoe
	Dimensions (in cm)
1-Removable roof	23,5 + e (depth) / 24 + 2 e (width)
2 et 3-Sides	20 (width) / 33 - e (front side) / 36 - e (back side)
4-Bottom	20 (depth) / 20 + 2 e (width)
5-Front with hole	33 (height) / 20 + 2 e (width) / Oval hole 65mm wide by 70mm high
6-Back	43 (height) / 20 + 2 e (width)

e is the thickness. If the board is 1.8 cm thick, then 2 e = 1.8 x 2 = 3.6 cm.

## Type 6
For Eurasian hoopoe, Eurasian scops owl, Stock Dove, common starling
	Dimensions (in cm)
1-Removable roof	19,5 + e (depth) / 22 + 2 e (width)
2 et 3-Sides	16 (width) / 33 - e (front side) / 35 - e (back side)
4-Bottom	16 (depth) / 16 + 2 e (width)
5-Front with hole	33 (height) / 16 + 2 e (width) / 90 mm diameter hole
6-Back	42 (height) / 16 + 2 e (width)

e is the thickness. If the board is 1.8 cm thick, then 2 e = 1.8 x 2 = 3.6 cm.

## Type 7
For tawny Owl
	Dimensions (in cm)
1-Removable roof	35 + e (depth) / 26 + 2 e (width)
2 et 3-Sides	22 (width) / 55 - e (front side) / 57 - e (back side)
4-Bottom	22 (depth) / 22 + 2 e (width)
5-Front with hole	55 (height) / 22 + 2 e (width) / 120 mm diameter hole
6-Back	64 (height) / 22 + 2 e (width)

e is the thickness. If the board is 1.8 cm thick, then 2 e = 1.8 x 2 = 3.6 cm.

# Assembly

1
2
3
Screws 40 mm
Screws 40 mm
Screws 40 mm
If you look from the side, there is a slight bevel on the front part (5). This is to be aligned with planks 2 and 3 on the side. Thus, once the roof is installed, everything is airtight. / The hole is made with a hole saw. / The hole is placed high to avoid falling chicks.

Screws 15 mm
We center the roof with 2 cm overhang on each side.
A hinge is installed on the roof and a clasp system for easy access for maintenance.

We pierce the bottom board and place pitons. This allows the wire to pass through.
6

# Material summary
## Wood
The wood is a class 3 untreated wood made to be outdoors.
## Hinge
1 hinge for the roof.
## Clasp
2 clasp systems on the sides of the roof. This allows easy opening for maintenance.
## Fasteners
Wood screws : 40 and 15 mm.
40 mm: about 20.
15 mm: about 6.
To avoid splitting, there are anti-splitting screws (or it is better to drill before screwing)
## Ion wire
1 to 2 m to hang the birdhouse.
## Material
- Tape measure
- Jigsaw
- Drill / screwdriver (with a hole saw)
# Details
Find details on https://habitat.seedtohumus.org/ concerning the heights, orientations, advice to avoid damaging the tree, maintenance...
# Questions ?
If you have any questions, go to https://habitat.seedtohumus.org/ and ask them in the article dedicated to the subject.
# Resources
Blueprints numbers 1, 2, 3, 4 and 5 are inspired by the Swiss Association for the Protection of Birds.
Blueprints numbers 6 and 7 are inspired by the LPO Drome Ardèche.